Maddie Powell, Aidan Levy, Lei Tapungot
Dr. Ludwick
MATH 447
4/5/2026

ChaCha20-Poly1305 Encrypted Chat

Abstract
This paper examines the design and implementation of an encrypted chat system using ChaCha20-Poly1305 and RSA-2048 key exchange. The purpose of the project is to demonstrate how encrypted communication protects messages in a client-server chat model where the server acts only as a relay between users. ChaCha20 is used to encrypt plaintext messages into ciphertext, while Poly1305 provides message authentication to verify that the ciphertext has not been modified during transmission. RSA-2048 is used during the initial key exchange phase so that clients can securely establish a shared symmetric session key before sending encrypted messages. The implementation was developed in Python and includes two versions: an encrypted version and a plaintext version. The plaintext version demonstrates the security weakness of sending messages without encryption, as the server can directly read and log client messages. In contrast, the encrypted version allows the server to see only ciphertext, nonce values, and authentication tags. By comparing these two systems, the project demonstrates the practical value of authenticated encryption in protecting confidentiality and integrity within digital communication systems.

Table of Contents

1. Abstract
2. Introduction
3. History
4. ChaCha20
5. Poly1305
6. AEAD Construction
7. System Design and Architecture
8. Implementation
9. Security Analysis
10. Performance and Comparison
11. Applications
12. Conclusion
13. Sources
Introduction
With the growth of digital communication in today’s digital landscape, security has become fundamentally required to protect the vast amount of personal data sent over networks. Specifically, chatrooms must preserve privacy during message exchanges between their clients. If they fail to do so, malicious entities may attack the network and possibly read, intercept, or modify private data.
To remedy this, end-to-end encrypted messaging systems are used. These systems ensure that only the sender and receiver can decrypt these messages. The server only works as a medium to relay messages between clients. The server does not have access to the original plaintext.
To implement this end-to-end system and protect data, two cryptographic algorithms are combined: ChaCha20-Poly1305. Together, they form Authenticated Encryption with Additional Data (AEAD). Originally designed by Daniel J. Bernstein, ChaCha20-Poly1305 has become a widely used mechanism to secure modern messaging systems. ChaCha20 is a stream cipher that encrypts messages using a shared key. Poly1305 is a message authentication code that allows a receiver to verify the source and that there have been no modifications to the data.
In this paper, we will examine the design of an end-to-end messaging system that utilizes ChaCha20-Poly1305. This paper aims to explore both algorithms individually, their behavior when combined within the AEAD framework, and analyze their security properties and performance as it pertains to secure communication.

History
Daniel J. Bernstein is a mathematician and cryptologist that created both the ChaCha20 and Poly1305. Poly1305 (the one-time authentication code) was created in 2005 as well as the Salsa20 cipher. Salsa20 was later refined to be the ChaCha20 cipher which was developed in 2008. In 2013 these algorithms were proposed to Internet Engineering Task Force (IETF) to use them in protocols like Transport Layer Security (TLS) and Datagram Transport Layer Security (DTLS). ChaCha20-Poly1305 was then standardized in RFC in 2015. In fact, google was impressed enough to implement ChaCha20-Poly1305 into Chrome 31 in November 2013. ChaCha20-Poly1305 is now required a cipher suite in TLS 1.3. Presently, ChaCha20-Poly1305 is used commonly in many protocols such as OpenSSH, WireGuard, and IPSec, and messaging applications.
        ChaCha20
The ChaCha20 is a stream cipher that was originally designed to substitute ciphers such as the Advanced Encryption Standard (AES). Unlike AES, ChaCha20 does not need hardware acceleration and is instead engineered to operate in constant time, making it more resistant to time based side-channel attacks.
ChaCha20 generates a pseudorandom keystream by applying a series of add-rotate-XOR (ARX) operations to an internal state. From a cryptographic viewpoint, this is very important because it avoids the use of lookup tables, which are frequently used in AES. As a result, ChaCha20 can achieve strong performance capabilities while maintaining constant time without any special effort, eliminating vulnerabilities that come with timing attacks. When compared to similar algorithms, ChaCha20 excels when encrypting large amounts of data. This data is most commonly VPNs or messages.
 ChaCha20 starts by making a 4x4 matrix of 32-bit words (512 bits total) composed of four constant words, eight key words (256 bit key), one block counter word, and three nonce words (96 bits). The block counter word is used to assist in producing distinct key stream blocks for each part of a message. A nonce is a unique number used in each encryption process. The nonce cannot be reused with the same key. Making sure that the nonce is different during each encryption process is an import part of keeping ChaCha20 secure.

The ChaCha20 algorithm operates in 10 double rounds (so 20 rounds, which is why it is called ChaCha20!). Due to ChaCha20 using 20 rounds of operations, this algorithm is strongly encrypted and resistant to attacks. Each round includes four column quarter rounds and four diagonal quarter rounds. A quarter round takes four 32-bit integers and implements a series of operations such as additions, XORs, and bitwise rotations. After these 20 rounds have finished, the final state is added back to the initial state, producing a 64-byte keystream. The ciphertext is then formed by XORing the keystream and plaintext. The decryption procedure mirrors the operations in the encryption process, sharing the same keystream and cipher stream. Therefore, to obtain the plaintext, it requires XORing the keystream and ciphertext.
        Poly1305
Poly1305 is a message authentication code (MAC) used to verify a message’s integrity and authenticity. It is a single use authenticator that requires a message and key (which cannot be reused) to create this message authentication code. Given a one-time 256-bit key, it initially generates two values: r and s. The message will then be divided into 128-bit blocks, where each block is processed sequentially. During this processing step, r is being used in the polynomial calculations to update a current value with accordance with the message, which is calculated by using modulo 2130 - 5.
After the blocks are processed, the resulting value will be combined with s to produce the message authentication code. The result will now be reduced to 128-bits, which gives the final message authentication code. Any modifications done to a message will result in a totally different authentication tag. Because of this property, Poly1305 can detect any modification they may have occurred.
The security in Poly1305 is reliant on the fact that the key should only be used once. When combined with ChaCha20, the concept is automatically satisfied. This happens because the first 32-bytes of ChaCha20’s keystream are what is used at Poly1305 one time key. What’s left over of the key stream is to be used to encrypt the original message.
AEAD Construction
Authenticated Encryption with Associated Data (AEAD) is a cryptosystem that provides both confidentiality and integrity for its ciphertext. It does this by encrypting a message with a key and nonce and verifying that it has not been modified using an authentication tag. The Authenticated Encryption with Associated Data construction supports the ChaCha20-Poly1305 algorithm. By combining verification and authentication into a single system, AEAD provides a tamper resistant and secure method for protecting transmitted data.
When using AEAD, ChaCha20 does the encryption piece, and Poly1305 does the authentication piece. AEAD takes in a 256-bit key, 96-bit nonce, a plaintext message of any length, and an optional Additional Authentication Data (AAD) of any length. ChaCha20-Poly1305 with AEAD starts where Poly1305 creates a one-time key by using ChaCha20 with the same key and nonce. The block counter is assigned 0. ChaCha20 is used for the one-time key by that it creates a 512-bit block, where the first 256-bit of that block is used for the key. The first 128-bits of those 512 bits are used to form r, and the next 128 form s. So, r and s together are the first 256-bits of the 512-bit block. The 256-bits that were not used will be discarded. Next, ChaCha20 will encrypt the plaintext (still using the same shared key and nonce). The initial counter is assigned 1. Lastly, the Poly1305 function is to be called with the key it had calculated, to undergo the authentication process. The authentication process involves the combination of AAD, ciphertext, and their lengths. Padding is also added in this process on a needs base to make sure data is arranged properly. The results will be the ciphertext (which always has equal length to the plaintext) and a 128-bit tag that came from Poly1305.
Decrypting the ciphertext is in parallel to the encryption process. It is just a matter of reversing the encryption process. Since XOR is its own inverse, the receivers XORs the ciphertext with the same keystream to recover the plaintext. Therefore, using the encryption from ChaCha20 will get the plaintext. Poly1305 does not calculate the authentication tag using the plaintext. It only uses the ciphertext and AAD (which is what it received). So, the newly created tag is compared to the received tag, for authentication purposes. If these tags match, then the message will be verified.
System Design and Architecture
An encrypted chat system uses a client-server model. It contains one central server and two or more clients. The server is only responsible for relaying the messages between the clients. The server does not have access to the plaintext as it is only relaying the ciphertexts, that only the clients can decrypt. With only decryption occurring on the client’s side, this demonstrates end-to-end encryption. The sender will encrypt the message before transmitting it. When the receiver receives the message, it must verify and decrypt the message.
There are two phases that occur in the protocol. The first phase is when clients generate RSA-2048 key pairs and exchange public keys through the server so that they can perform an asymmetric key exchange. An asymmetric key exchange is when a public key and private key are used together to transmit data securely. Combing ChaCha20-Poly1305 and RSA is useful because RSA is great for securing shared keys, while ChaCha20-Poly1305 is fast at encrypting messages. Each client will generate their own key pair. Each client will then share its public key to the server. Once a peer’s public key is known, one client generates a 256-bit ChaCha20-Poly1305 session key and encrypts that session key with the recipient’s RSA public key before sending it through the server. A symmetric key is a single key that is shared between clients to encrypt and decrypt messages. In the second phase, all messages will be encrypted using ChaCha20-Poly1305 along with a unique 96-bit nonce created for each message. The ciphertext and the authentication tag are sent through the server to the receiver. The server only has access to seeing the byte stream and cannot decrypt any messages.
Implementation
The implementation of this project was completed using Python and was divided into two versions. The first version is the encrypted chat system, which uses RSA-2048 for key exchange and ChaCha20-Poly1305 for message encryption and authentication. The second version is a plaintext chat system, which was created for comparison purposes during our live demonstration. The plaintext version shows what happens when messages are sent through a server without encryption. In that case, the server has direct access to reading the messages that clients send. By implementing both versions, the project demonstrates the practical difference between an unsecured chat application and an end-to-end encrypted chat application.
The encrypted version is organized around these three main components: the chat client, the chat server, and the cryptographic helper modules. The ChatClient.py file handles the user interface, client connection, key exchange, encryption, decryption, and message sending. The ChatServer.py file accepts client connections, tracks connected users, distributes public keys, and relays encrypted packets between clients. The cryptographic functions are separated into ChaCha.py and RSA.py. Our group chose not to implement the code behind the ChaCha20-Poly1305 and RSA-2048 algorithms since they already exist in libraries, and we would risk coding errors which could be fatal to the encryption of the messages. This separation makes the implementation easier to understand because the network logic and cryptographic are not placed into one file. The client and server communicate using JSON packets over TCP sockets, where each packet contains a type field that tells the program how to process the message. For example, packets may represent a new client joining, a key exchange message, or an encrypted chat message.
When a client starts, it generates an RSA key pair and sends its public key to the server. The server stores the public key and shares it with other connected clients. The server also sends a proof message encrypted with the clients’ public key to confirm that the RSA exchange is working correctly. After this, the client sends a confirmation message back to the server. This handshake does not encrypt actual chat messages by itself; instead, it allows clients to securely exchange the symmetric key that will later be used for ChaCha20-Poly1305 encryption. The RSA module uses a 2048-bit RSA key pair and OAEP padding to encrypt and decrypt the exchanged key material. The RSA helper class creates a private and public key pair, exports public keys, encrypted plaintext using another user’s public key, and decrypts received ciphertext using the client’s private key.
Once clients know each other’s public keys, one client generates a ChaCha20-Poly1305 session key. This key is created as 32 random bytes, which matches the 256-bit key requirement for ChaCha20-Poly1305. The key is then Base64 encoded so that it can be safely placed inside a JSON packet. The client encrypts this session key with the other client’s RSA public key and sends it through the server as a key_exchange packet. The server does not decrypt this session key. Instead, it only forwards the encrypted key exchange packet to the intended client. Furthermore, when the receiving client gets this packet, it decrypts the session key with its own RSA private key and stores it for later encrypted communication. This allows the clients to establish a shared symmetric key while preventing the server from seeing the final ChaCha20-Poly1305 key.
After the session key is established, all normal chat messages are sent using ChaCha20-Poly1305. When the user types a message, the client first encodes the plaintext as bytes. Then the ChaChaCipher class creates a ChaCha20-Poly1305 cipher object using the stored 256-bit key. The encryption function produces three important values: a nonce, the ciphertext, and an authentication tag. These values are Base64 encoded and sent through the server as an encrypted chat packet. The server receives the packet, but it only sees the nonce, ciphertext, and tag. It cannot read the original plaintext because the plaintext has already been encrypted before leaving the sender’s client. The server’s role is therefore limited to routing the encrypted packet to the correct recipient.
On the receiving side, the client reverses this process. When the recipient receives an encrypted chat packet, it looks up the session key associated with the sender. The client then decodes the nonce, ciphertext, and tag from Base64 and passes them into the ChaCha20-Poly1305 decryption function. The decrypt_and_verify function performs two tasks at once: it decrypts the ciphertext and checks the Poly1305 authentication tag. If the tag is valid, the message is accepted and displayed to the user. If the tag does not match, then the message is rejected because it may have been modified or corrupted. This directly demonstrates the AEAD property of ChaCha20-Poly1305 because the same operation protects both confidentiality and integrity.
The server in the encrypted version was intentionally designed so that it cannot access plaintext messages. In the encrypted_chat packet handler, the server extracts the sender name, target client ID, nonce, ciphertext, and tag. It then constructs a relay packet and send that packet to the target client. The server log displays the ciphertext instead of the original message. This was an important design decision because it demonstrates end-to-end encryption. Even though the server is necessary for communication, it is not trusted with message contents. The encrypted server also rejects plaintext chat packets, showing that the secure version is designed to avoid accidental plaintext communication.
The second version of the program was created as a plaintext comparison. This version uses a similar client server structure, but it removes the RSA and ChaCha20-Poly1305 layers. The plaintext client sends a normal JSON packet containing the message directly in a message field. The plaintext server receives the packet, reads the message, logs it, and broadcasts the same message to the other connected clients. This means the server has full access to the original message contents. The plaintext version is useful because it provides a direct comparison against the encrypted version. In the plaintext implementation, the server log can display the sender’s name and message exactly as written. In the encrypted implementation, the server can only display unreadable ciphertext.
Security Analysis
ChaCha20-Poly1305 offers several security properties that make it appealing to use when securing messages in messaging software. When using an Authentication Encryption with Associated Data
Performance and Comparison
This is the performance and comparison section
Applications
This is the application section
Conclusion
This is the conclusion
Sources